## Slide 1: Proposed Lead and Copper Rule Improvements
Overview and Key Provisions

## Slide 2: Presented on 1/16/24 by:
Seth Kramer Lead and Copper Monitoring Team
512-239-6167 seth.kramer@tceq.texas.gov
Presentation Outline:
Introduction
Overview
Key Provisions
Resources
Q&A

## Slide 3: Introduction
Presentation Purpose:
Inform on EPA’s proposal to improve the LCR
Highlight the key provisions of the proposed LCRI
Share EPA resources

## Slide 4: Overview
Key Events:
Compliance date for the LCRR - October 16, 2024
Proposed LCRI announced - November 30, 2023
Final LCRI - expected before October 16, 2024
Compliance date for LCRI - 3 Years after publication date

## Slide 5: LCRR Requirements
Upcoming Activities:
Initial service line inventory due by 10/16/24
Public notice
  To customers with lead, GRR, and unknown SLs within 30 days of LSLI submission and annually by July 1
  Tier 1 notice (within 24-hours of an ALE)

## Slide 6: Key Provisions of the Proposed LCRI (1)
Lead Service Line Inventories
Initial inventory by October 16, 2024
Baseline inventory (includes connectors)
  By LCRI compliance deadline
  Updated annually
  Create a replacement plan
  Identify unknown SL materials
Inventory validation (of subset of non-lead service lines)
  3 Years before 10 yr. deadline (or deferred deadline)
  Required for non-lead lines identified by method other than:
    Records review (listed in rule)
    Two-point inspection

## Slide 7: Key Provisions of the Proposed LCRI (2)
100% Lead Service Line Replacement
Most water systems must replace LSLs within a 10 yr. deadline
Deadline deferment criteria
  > 100,000 lead/GRR - 10,000 per year
  > 39 lead/GRR per 1,000 household
Replacement requirements
  Fully replace lead and GRR

## Slide 8: Key Provisions of the Proposed LCRI (3)
Improving Tap Sampling
  Site with LSL – 1st and 5th liter samples
  Use the highest value to determine compliance

## Slide 9: Key Provisions of the Proposed LCRI (4)
Lowering the Lead Action Level
Eliminate LCRR trigger level
Lower action level from 15 µg/L to 10 µg/L
ALE requirements
  Inform the public
  Take action to reduce lead exposure
  Concurrently work to replace all LSLs
  Install or adjust CCT

## Slide 10: Key Provisions of the Proposed LCRI (5)
Deferment of OCCT and Re-Optimized OCCT Processes
  If removal of 100% of lead and GRR service lines can be replaced at 20% per year over 5 years

## Slide 11: Key Provisions of the Proposed LCRI (6)
Strengthening Protections to Reduce Exposure
  Multiple ALE systems
    Conduct additional outreach
    Make filters available to all consumers

## Slide 12: Key Provisions of the Proposed LCRI (7)
Improved Public Education Requirements
  Updated content and delivery frequency
  Proactive messaging about lead in drinking water

## Slide 13: EPA Resources
EPA Proposed Lead and Copper Rule Improvements webpage
https://www.epa.gov/ground-water-and-drinking-water/proposed-lead-and-copper-rule-improvements
Federal Register - National Primary Drinking Water Regulations for Lead and Copper: Improvements (LCRI)
https://www.federalregister.gov/documents/2023/12/06/2023-26148/national-primary-drinking-water-regulations-for-lead-and-copper-improvements-lcri

## Slide 14: Questions?

## Slide 15: Link to Survey to Provide Feedback on LCRR/Proposed LCRI as of January 16, 2024
https://forms.office.com/r/72Ei4dKqYy