## Slide 1: Monitoring Requirements: AMOCs, Case-by-Case Permits, and Title V Permits
Rhyan Stone, Manager
Operating Permits Section

## Slide 2: Monitoring Requirements Overview
Alternative monitoring requirements
Periodic Monitoring (PM)
  40 CFR Part 70 and 30 TAC Chapter 122
Compliance Assurance Monitoring (CAM)
  40 CFR Part 64 and 30 TAC Chapter 122
Permit by Rule Supplemental Tables
Notes: Monitoring is required to demonstrate compliance with all emission limits and/or standards and is included in permits through a few different means. For example, monitoring is included in NSR permits within the permit’s special terms and conditions. For Title V permits, monitoring requirements are included in the terms and conditions, applicable requirements summary table, and additional monitoring tables as applicable.
AMOCs are used whenever there is a deviation from regulatory monitoring requirements. AMOCs are included within a site’s Title V permit.
PM is required by 40 CFR Part 70 and 30 TAC Chapter 122. PM is needed for an emission unit subject to an emission limitation or standard, unless the rule includes “periodic monitoring (which may consist of recordkeeping) sufficient to yield reliable data from the relevant time period that are representative of the emission unit’s compliance with the applicable requirement, and testing, monitoring, reporting, or recordkeeping sufficient to assure compliance with the applicable requirement” (30 TAC § 122.602(b)). Some, but not all, categories of rules that contain adequate periodic monitoring language are listed in 30 TAC § 122.602(b)(1)-(4).
CAM is required by 40 CFR Part 64 and 30 TAC Chapter 122. CAM is needed for an emission unit that satisfies three criteria: unit is subject to an emission limit or standard, unit uses a control device to meet that limit/standard, and unit’s pre-control potential to emit (PTE) of the pollutant in the limit/standard is greater than or equal to the major source threshold for that pollutant. 30 TAC § 122.604(c)-(d) list situations where CAM does not apply. A given rule may contain monitoring that satisfies CAM requirements.
PBR monitoring requirements are incorporated by reference in the Title V permit through the use of the OP-PBRSUP
One example from the PM/CAM exemptions in 30 TAC § 122.602(b)(1)-(4) and 30 TAC § 122.604(c)-(d) is rules that were proposed by EPA after November 15, 1990. These rules will have adequate monitoring language in the regulatory citations.

## Slide 3: AMOC Overview
How to submit an AMOC
What is required for AMOC Review/Approval
AMOC processing

## Slide 4: AMOC Submittals
AMOC requests should be submitted to TCEQ by email (APD, Anne Inman, and the appropriate region).
Requests should also be sent to any relevant local programs and to EPA for major sites.
Separate requests require separate documentation.
Requests must include a cover letter and attachments with details to support and justify the request.
Notes: AMOC Submittals
  Submit AMOC request to TCEQ – Air Permits Division (APD) & REGION + LOCAL + Environmental Protection Agency – EPA [Region 6 (R6), Office of Air Quality Planning and Standards (OAQPS)]
  Each request stands-alone (documentation)
  Must have all needed information to satisfy delegated Administrator or Executive Director
  If major site, signed by Responsible Official (RO)/Duly Authorized Representative (DAR)
  Cover letter with overview of request

## Slide 5: AMOC Review
We suggest discussing the request prior to official submittal.
To facilitate the review, ensure the project identifies:
  Site and plant type
  Sources, units, and controls
  State and federal regulations
  NSR and Title V authorizations
  Justification for the alternative
Determine affected NSR, Title V, or enforcement actions and the timing of the AMOC.
Notes: AMOC Review
  Reach out to us (Anne Inman) to discuss your request prior to submitting the official request. This can help streamline the process and ensure the review of the request goes smoothly.
  The official request needs to include the information on the slide. This information helps provide context for the request and helps us identify what other actions will be required as a result (i.e. NSR or Title V permit actions)
  Justification for the request can include real world conflicts, monitoring data, manufacturer’s specifications, emissions calculations, and so on.

## Slide 6: AMOC Processing
Application
  Situation and facility information
  Applicable rules
  Justification
Technical Review
  Confirm citations and historical determinations
  Evaluate justifications
  Draft to NSR, Title V, Region, and Local Programs, depending on scope
  Input from EPA
Final Action
  Approval or denial letter and, if applicable, a plan
Notes: Processing for most AMOCs
Application process:
    Situation & facility information
    Applicable rules
    Justification
Technical review process:
      Confirm citations & historical determinations
      Evaluate justifications
      Draft to Region & Local
      Input from EPA
Action process: Approval or denial letter & (possible) plan

## Slide 7: Case-by-Case and Title V Permits
Boilerplate and pre-approved options
  NSR terms and conditions
  Title V PM and CAM options
  Justification may be required for PM and/or CAM deviation limits.
Site specific monitoring
  Monitoring that deviates from pre-approved language or options
  Justification must be provided
Notes: Note the theme, any case-by-case or site-specific monitoring requires justification. We have boiler plate language and pre-approved monitoring options to streamline our review and reduce application processing timelines. Site-specific monitoring requires additional review, and the review time will depend on response times to requests for information (and whether appropriate information is provided).

## Slide 8: Deviation Limits
Deviation Limits
  Manufacturer’s specifications/recommendations
  Historical data
  Specificity – Specific numerical values are preferred
  Additional Changes
Notes: Justification should be provided for deviation limits and can include manufacturer’s specifications or recommendations and/or historical data.
Specific data is preferred and can reduce the back and forth during review. Specific data also reduces the chance of public/EPA comments. Several of the comments we’ve received have targeted monitoring sufficiency and insufficient justification.
Deviation limits may be updated for clarity. This may include simplifying language or making the limit less ambiguous.

## Slide 9: Deviation Limit Example – Pressure Drop
Stationary vent subject to 30 TAC Chapter 111, Visible Emissions
Controlled by a fabric filter and needs PM
Proposes case-by-case PM monitoring of pressure drop on a daily basis
“Minimum 2 in. w.c., maximum 6 in. w.c.” for the deviation limit
Notes: As an example of deviation limit justification, consider a vent subject to 30 TAC Chapter 111, Visible Emissions. To comply with the opacity limit, the vent is controlled by a fabric filter. Case-by-case PM is being added where pressure drop will be monitored daily. The proposed deviation limit has a minimum of 2 inches and maximum of 6 inches water column. Applicant needs to provide information supporting these values. Performance test data showing pressure drop and opacity over the test runs could be submitted. If there is manufacturer’s literature specifying minimum and maximum pressure drop for operating this fabric filter, that could be provided. It should also indicate that the unit would achieve the necessary particulate control/opacity in that range. The site could also provide historical data showing that when this fabric filter is operating, opacity has consistently met the limit in the regulation when operated within the specified minimum and maximum pressure drop values.

## Slide 10: Pressure Drop Deviation Limit Justification
Possible justifications for the minimum and maximum pressure drop:
  Performance test data – provide an excerpt from the stack test report showing pressure drop and opacity over test runs
  Manufacturer’s recommendations – provide an excerpt from vendor literature indicating the pressure drop range and control performance/resulting opacity
  Historical data – provide operating data from the site showing measured pressure drop and opacity
Notes: As an example of deviation limit justification, consider a vent subject to 30 TAC Chapter 111, Visible Emissions. To comply with the opacity limit, the vent is controlled by a fabric filter. Case-by-case PM is being added where pressure drop will be monitored daily. The proposed deviation limit has a minimum of 2 inches and maximum of 6 inches water column. Applicant needs to provide information supporting these values. Performance test data showing pressure drop and opacity over the test runs could be submitted. If there is manufacturer’s literature specifying minimum and maximum pressure drop for operating this fabric filter, that could be provided. It should also indicate that the unit would achieve the necessary particulate control/opacity in that range. The site could also provide historical data showing that when this fabric filter is operating, opacity has consistently met the limit in the regulation when operated within the specified minimum and maximum pressure drop values.

## Slide 11: Deviation Limit Example - Temperature
Loading rack subject to 30 TAC Chapter 115
Controlled by a vapor combustor and needs CAM
Option CAM-VC-002 (temperature monitoring, 4 times per hour)
Applicant selects “Minimum temperature of 1100 °F” for the deviation limit
Notes: As an example of deviation limit justification, consider a loading rack subject to 30 TAC Chapter 115, Subchapter C, Division 1 (Loading and Unloading of VOCs). Emissions are routed to a vapor combustor for control. The unit meets criteria for CAM and is a large CAM unit. The applicant selects option CAM-VC-002 from TCEQ guidance, which requires monitoring the combustion temperature at least four times per hour. Applicant identifies minimum temperature of 1100 F for deviation limit. Justification could be a portion from the most recent stack test showing temperatures and measured VOC concentration. Another suggestion would be an excerpt from the manufacturer’s literature showing that the combustor will achieve the required control performance at temperatures consistent with the minimum value.

## Slide 12: Temperature Deviation Limit Justification
Possible justifications for temperature:
  Performance test data – provide an excerpt from the stack test report showing temperature and VOC concentration
  Manufacturer’s recommendations – provide an excerpt from vendor literature indicating control performance at/above the minimum temperature
Notes: As an example of deviation limit justification, consider a loading rack subject to 30 TAC Chapter 115, Subchapter C, Division 1 (Loading and Unloading of VOCs). Emissions are routed to a vapor combustor for control. The unit meets criteria for CAM and is a large CAM unit. The applicant selects option CAM-VC-002 from TCEQ guidance, which requires monitoring the combustion temperature at least four times per hour. Applicant identifies minimum temperature of 1100 F for deviation limit. Justification could be a portion from the most recent stack test showing temperatures and measured VOC concentration. Another suggestion would be an excerpt from the manufacturer’s literature showing that the combustor will achieve the required control performance at temperatures consistent with the minimum value.

## Slide 13: Case-by-Case Monitoring Submittals
Justification
  Detailed emission calculations
  Changing monitoring frequency
  Ensuring compliance with emission limits or standards
Monitoring frequencies
  PM – must be consistent with other regulations and permit requirements
  CAM- Large CAM units require monitoring four times per hour, and small CAM units require monitoring once per day.
Averaging Period
Notes: Justification for CBC submittals should include detailed emission calculations, justification for changing monitoring frequency when comparing with other pre-approved options of frequencies specified in other regulations for the same type of source/pollutant/control device.
Justification should also describe how the monitoring will assure compliance with the applicable emission limit or standard. The proposal should also specify any monitor calibration/accuracy requirements as required.
PM – Monitoring frequency must be consistent with other regulations and permit requirements for the unit (all credible data). The minimum frequency for PM is once per year unless other permit requirements require more frequent monitoring.
CAM – Large CAM units require a monitoring frequency of at least 4 times per hour, and small CAM units require at least once per day.
Averaging periods – Must be justified if not specified in the regulation and cannot be used to avoid reporting deviations
PM/CAM submittals must be submitted using form OP-MON
Guidance for Title V Permits (including PM and CAM guidance) can be found at Permitting Tools and Guidance for Site Operating Permits - Texas Commission on Environmental Quality - www.tceq.texas.gov

## Slide 14: Case-by-Case Example – 30 TAC Chapter 117
Process heater subject to 30 TAC Chapter 117, Subchapter B
Proposal requests monitoring of fuel flow rate at a monthly frequency
Applicant selects a fuel flow rate for the deviation limit
Notes: An example for a justification for a deviation limit for the CO limit in 30 TAC Chapter 117, Subchapter B:
The applicant has chosen to monitor the Fuel Flow Rate or Heat Input at a monthly frequency to comply with the 400 ppmv @ 3% O2, Dry CO emission limitation in 30 TAC Chapter 117, Subchapter B.
They select a maximum Fuel Flow Rate or Heat Input for the deviation limit.
The following justification needs to be provided:
data on how the maximum Fuel Flow Rate or Heat Input was determined. This can be derived from stack tests, measured emissions, performance data, NSR authorizations, etc.
justification/data/calculations showing how the Fuel Flow Rate or Heat Input correlates to the emission limit from the rule. In this case, in units of PPMV @ 3% O2, Dry.
Actual values should be used in the justification/data/calculations, and all terms/variables should be defined (how you got them).
The calculations should start with the Fuel Flow Rate or Heat Input and end in the units from the emission limit from the rule, showing how the deviation limit correlates to the emission limit and how it shows reasonable compliance with the emission limit from the rule.

## Slide 15: 30 TAC Chapter 117 - Deviation Limit Justification
Possible justifications:
  Data showing how the maximum fuel flow rate was determined (stack test data, emission data, performance data, etc.)
  Data or calculations showing how the fuel flow rate correlates to the emission limit from the rule
Notes: An example for a justification for a deviation limit for the CO limit in 30 TAC Chapter 117, Subchapter B:
The applicant has chosen to monitor the Fuel Flow Rate or Heat Input at a monthly frequency to comply with the 400 ppmv @ 3% O2, Dry CO emission limitation in 30 TAC Chapter 117, Subchapter B.
They select a maximum Fuel Flow Rate or Heat Input for the deviation limit.
The following justification needs to be provided:
data on how the maximum Fuel Flow Rate or Heat Input was determined. This can be derived from stack tests, measured emissions, performance data, NSR authorizations, etc.
justification/data/calculations showing how the Fuel Flow Rate or Heat Input correlates to the emission limit from the rule. In this case, in units of PPMV @ 3% O2, Dry.
Actual values should be used in the justification/data/calculations, and all terms/variables should be defined (how you got them).
The calculations should start with the Fuel Flow Rate or Heat Input and end in the units from the emission limit from the rule, showing how the deviation limit correlates to the emission limit and how it shows reasonable compliance with the emission limit from the rule.

## Slide 16: Permit by Rule Supplemental Table (OP-PBRSUP)
Completing the form
  Table A – Include all units authorized by registered PBRs. Each unit should be listed on its own line. Include the registration number, PBR number, and registration date.
  Table B – Include all units authorized by claimed PBRs. Include the PBR number and version number.
  Table C – Include all PBR authorizations for insignificant sources.
  Table D – Include the monitoring, recordkeeping, or reporting that demonstrates compliance with the PBR for each unit identified on Tables A and B.
Notes: PBRSUP
Table A is for documenting registered PBRs. Registration numbers are included in the Title V permit in the New Source Review Authorization Reference by Emission Unit Table. For this table, be sure to list the registration issuance date instead of the PBR version no.
Table B is for documenting all claimed PBRs (except PBRs included on Table C). Include the version number of the PBR being claimed
Table C is for documenting claimed PBRs for insignificant sources. Any PBRs included on the table in the form instructions are required to be listed on Tables A or B. PBRs not named in the form instructions should be listed on Table C. The form instructions can be found at TCEQ Form 20875 - Permit By Rule Supplemental Table
Table D is for documenting the MRRT that is conducted to demonstrate compliance with the PBR(s). All entries on tables A or B must have an associated entry on table D.
All PBRs for the permit area must be identified on the PBRSUP, including PBRs that authorize units not included in the permit. If a site has multiple Title V permits, only the PBRs that authorize the specific application area need to be identified.

## Slide 17: OP-PBRSUP Monitoring Sufficiency
Common Issues
  Insufficient justification or vague requirements
  Missing required information or “N/A”
  Missing units/PBRs
Recommendations
  Be specific
  Be consistent
Notes: PBRSUP Monitoring
Common issues:
-Insufficient justification or vague requirements: The monitoring identified in table D may not provide specific justification or requirements that assure compliance with the PBR.
-Missing required information: N/A or leaving the column blank is not accepted. MRRT must be included for each unit/PBR included on tables A or B. If the PBRs identified on tables A or B do not include a specific emission limit or standard, the monitoring in table D should assure compliance with the general limits outlined in 106.4.
-Missing units or PBRs: Be sure to include entries for all units/PBRs included on Tables A or B. Units/PBRs included on table C should not be listed in table D
In the past, these issues have resulted in public and/or EPA comments.
Recommendations:
-Be specific: Try to be specific with what MRRT is conducted to demonstrate compliance with the PBR. Use the periodic monitoring guidance found at periodicmon.pdf as a starting point. Include the specific parameters that are monitored or the specific records that are kept. For example, instead of “Maintain throughput for tank” include specifics on why this ensures compliance (i.e. frequency of throughput estimates/records and emission calculation to ensure emission limit is met).
-Be consistent: Be sure that the monitoring identified on table D is consistent (both with other similar units identified on the form and with requirements established for the unit elsewhere in the permit).

## Slide 18: Questions?
Rhyan Stone
  Email: rhyan.stone@tceq.texas.gov
  Phone: (512) 239-1293
General Questions
  Email: airperm@tceq.texas.gov
  Phone: (512) 239-1250