## Slide 1
Beneficial Reuse of Biosolids in Texas
The reuse of biosolids as fertilizer for farming in Texas has several benefits, including:
  Serves as ready source of nutrients for plant growth
  Reduces use of chemical fertilizers
  Reduces costs for sewage treatment facilities
  Reduces disposal of biosolids in landfills
Definition of Biosolids: Sewage sludge that has been treated or processed to meet Class A, Class AB, or Class B pathogen standards under Texas Administrative Code Chapter 312 for beneficial use.

## Slide 2
  The Texas Commission on Environmental Quality (TCEQ) has rules in place (Texas Administrative Code Part 30, Section 312) that provide guidance for the beneficial reuse of biosolids while maintaining public safety.
Treatment standards are set so that biosolids are safe when applied to the land
Pollutant limits are set for biosolids applied to land
Regulatory agencies are notified or require a permit or registration for biosolid applications
Management practices for safe reuse are defined
TCEQ provides oversight for reuse of biosolids
How Does TCEQ Ensure the Reuse of Biosolids is Safe?

## Slide 3
Treatment and Classification of Biosolids

## Slide 4
How Does Sewage Sludge Become a Biosolid?
Sewage sludge
Treatment
Biosolid
Solid, semi-solid, or liquid residue generated during the treatment of domestic sewage in treatment works.
Sewage sludge that has been treated or processed to meet Class A, Class AB, or Class B pathogen standards for beneficial use.
Stabilize, reduce viruses/bacteria, and limit appeal to rodents, insects, etc.
Figure 1. Definitions of sewage sludge, treatment, and biosolids (Sect. 312.8)

## Slide 5
How Are Biosolids Classified? What Do the Classifications Mean?
 | Treatment Process for Pathogens | Bacteria Levels
Class A | Pathogen Treatment Alternatives 1, 5, or 6 | Fecal coliform < 1000
Class AB (incorporated) | Pathogen Treatment Alternatives 2 thru 4 | Fecal coliform < 1000
Class AB | Pathogen Treatment Alternatives 2 thru 4 | Fecal coliform< 1000
Class B | Alternatives 5 or 6 with additional requirements | Fecal coliform < 2 million
Higher levels of pathogens

## Slide 6
How are Biosolids Treated for Bacteria, Viruses, and Other Organisms (Pathogens)?
Pathogen Treatment Alternative | Description
1 | Raise temperature for a specific time period which is determined by percent solids
2 | Raise temperature above 52 oC for at least 12 hours within time pH is raised above 12 for 72 hours. Then air dry biosolids to reach 50% solids
3 | Prior to pathogen treatment, determine whether biosolids contain viruses or eggs of parasitic worms and use to determine classification either before or after treatment
4 | Prior to pathogen treatment, determine whether biosolids contain viruses or eggs of parasitic worms and use to determine classification
5 | Federal Process to Further Reduce Pathogens (PFRP)
6 | EPA-approved alternative process approved as equivalent to PFRP
Pathogen treatment requirements in Sect. 312.82

## Slide 7
How are Biosolids Treated to Minimize Attraction of Rats, Rodents, etc. (Vectors)?
Pathogen Treatment Alternative* | Description
1 | Reduce mass of volatile solids by a minimum of 38%
2 | Demonstrate specific properties by bench-scale test for 40 days
3 | Demonstrate specific properties by bench-scale test for 30 days for liquid portion of biosolids
4 | Measure specific oxygen uptake rate (SOUR). Goal is less than 1.5 mg of oxygen per hour per gram solids
5 | Treat in aerobic process for 14 or more days where temperature on average is >45 oC and minimum is 40 oC
6 | Raise pH to 12 or higher by alkali addition for 2 hours and 11.5 for an additional 22 hour
7 | 75% or more of the solids in biosolids may not contain unstabilized solids prior to mixing
8 | 90% or more of the solids in biosolids may contain unstabilized solids prior to mixing
9 | Inject biosolids below land surface
10 | Incorporate biosolids into the soil within 6 hours
12 | The pH should be raised to 12 or higher by alkali addition and maintained for 30 minutes
Vector treatment requirements in Sect. 312.83
* Alternative 11 does not apply to land application of biosolids and was intentionally skipped.

## Slide 8
For Which Land Uses are the Treatment Approaches to Minimize Attraction of Rats, Rodents, etc. (Vectors) Applied?
Pathogen Treatment Alternative | Agricultural, forest, public contact, or reclamation property | Lawn, home, or garden properties | Sold or given away in bags | Domestic septage
1 | X | X | X | 
2 | X | X | X | 
3 | X | X | X | 
4 | X | X | X | 
5 | X | X | X | 
6 | X | X | X | 
7 | X | X | X | 
8 | X | X | X | 
9 | X |  |  | X
10 | X |  |  | X
12 |  |  |  | X
Vector treatment requirements in Sect. 312.83
* Alternative 11 does not apply to land application of biosolids and was intentionally skipped

## Slide 9
Application Limits and Pollutant Limits in Biosolids

## Slide 10: How Are Limits on the Amount of Biosolids Estimated?
Biosolids are a source of nitrogen to improve crop growth. The amount applied is limited to the amount needed for crop growth.
The amount of nitrogen needed for a specific crop is estimated as:
=
Estimate nitrogen needed for planned crop yield (varies by crop and how much will be grown)
Measure/estimate available nitrogen in the soil (0 to 6 inches and 6 to 24 inches)
Difference is the amount of nitrogen need to be added from biosolids
Management requirements in Sect. 312.44

## Slide 11
What Are the Pollutant Limits for Biosolids?
Metals | Maximum Concentration (milligrams per kilogram) for | Average Concentration (mg/kg) | Cumulative metal loading (kilograms per hectare) | Annual Metal Loading Rate (kilograms per hectare)
Arsenic | 75 | 41 | 41 | 2
Cadmium | 85 | 39 | 39 | 1.9
Chromium | 3000 | 1200 | 3000 | 150
Copper | 4300 | 1500 | 1500 | 75
Lead | 840 | 300 | 300 | 15
Mercury | 57 | 17 | 17 | 0.85
Molybdenum | 75 | monitor | monitor | monitor
Nickel | 420 | 420 | 420 | 21
Selenium | 100 | 36 | 100 | 5
Zinc | 7500 | 2800 | 280 | 140
Polychlorinated Biphenyls | 50 | -- | -- | --
Metal limits in Sect. 312.43

## Slide 12
Permits, Registrations, and Notifications

## Slide 13
How Does TCEQ Know Who is Applying Biosolids?
TCEQ requires businesses that sell or apply biosolids to provide information so they can make sure land application of biosolids follows regulations. TCEQ requires different types of information to be sent to them depending on the biosolids being applied.
Permits are required to use Class B biosolids on farmland
Notifications are required for generators who plan to store, land apply, or market and distribute biosolids
Registrations are required to use Class A biosolids, Class AB biosolids, water treatment residuals, or domestic septage on farmland that does not meet metals, pathogen, or vector control requirements

## Slide 14
What Information is Required on a Permit to Apply Class B Biosolids?
TCEQ requires permits to use Class B biosolids on farmland. Permits require approval from TCEQ prior to applying biosolids and include the following information:
Owner/operator of treatment facility or owner of the application site (if biosolids from outside Texas)
A map showing application area boundaries
List of property owner(s), with an affidavit stating each property owner(s) has agreed to the land application
List of landowners and addresses within ¼ mile of application area, as well as landowners adjacent to the property
Maximum amount of biosolids to be applied
Soil sample results that measure metals and nutrients prior to application
Information on surface water and groundwater within ¼ mile
Nutrient management plan to protect surface water (if in a major sole-source impairment zone)
Proof of Liability or Environmental Impairment Insurance
Permit requirements in Sect. 312.11

## Slide 15
What Information is Required to Register a Land Application Area?
Registration is required to use Class A biosolids, Class AB biosolids, domestic septage, or water treatment residuals on farmland that meet certain requirements. Registration provides information that allows TCEQ to track where and when these biosolids are used. Registration includes the following information:
Description and composition of material to be used on farmland
Description of processes generating the biosolids
Information about the site and planned management of the biosolids
List of property owner(s) where the material is to be applied
A description of the beneficial use of the biosolids
List of landowners and addresses within ¼ mile of application area and landowners adjacent to the property
Soil characteristics and subsurface conditions at each application unit
Registration requirements in Sect. 312.12

## Slide 16
What Information is Required on a Notification to Apply Biosolids?
Notifications by generators to distribute biosolids (except Class B) provide information that allows TCEQ to track where and when biosolids were applied.
  Where the biosolids were generated (which treatment facility)
  Who will receive the biosolids
  Description of marketing and distribution plan
    Plans to sell or give away biosolids and general proposed uses
    Methods for distributing, marketing, handling, and transporting
    Expected quantity to be sold
    Storage methods to prevent surface water runoff and contamination of groundwater
  Maps showing buffer zone areas for persons who receive Class AB biosolids
  Adverse weather plan
Activities can begin 30 days after notification if TCEQ doesn’t raise an objection.
Notification requirements in Sect. 312.4

## Slide 17
Management Practices

## Slide 18
What Management Requirements Are in Place for Application of Biosolids?
 | Specific Requirements By Class
Class A | Core Requirements
Class AB (incorporated) | Core Requirements only if mixed into soil
Class AB | Core Requirements plus the following: Post signage at application sites Buffer zones to odor receptors Staging of biosolids away from odor receptors Best Management Practices (BMPs) to address tracking biosolids off-site
Class B | Core requirements Post signage at application sites Buffer zones to odor receptors Staging of biosolids away from odor receptors BMPs to address tracking biosolids off-site Additional restrictions on next slide.
Core Requirements
Prohibit land application during rain or on to saturated soil Require cover on trucks Prohibit creating nuisance conditions (trash, odors, dust, and off-site tracking) Submit an adverse weather and alternative plan Apply when land slopes are less than 8% Do not apply in a designated floodway
Management requirements in Sect. 312.44

## Slide 19
Additional Requirements When Using Class B Biosolids
  Above-ground food crops like lettuce may only be harvested 14 months after treatment
  If biosolids are at the surface for less than 4 months before mixing in soil, below-ground food crops like carrots may only be harvested 38 months after application
  If biosolids are at the surface for 4 months or longer, below-ground food crops like carrots may only be harvested 20 months after application
  Food, feed, and fiber crops may only be harvested 30 days after application
  Domestic livestock may not graze within 30 days of application
  Turf may only be harvested 1 year after application if turf is used for residences or public access areas. If access to turf is low, turf may be harvested after 30 days
Pathogen treatment requirements in Sect. 312.82

## Slide 20
When are Buffer Zones Required?
  Buffer zones are required when biosolids applied to land are Class AB or Class B (not Class A) or when domestic septage is applied to land.
  Buffer zones are identified during the permit or registration process.
  Buffer zone requirements are defined on the next page
Management requirements in Sect. 312.44

## Slide 21
What are the Buffer Zone Requirements for Class AB or Class B Biosolids or Domestic Septage?
 | Buffer Zone for Class AB, Class B, or Domestic Septage
Surface water | 200 feet if biosolids are not incorporated into soil OR 33-foot vegetative buffer if biosolids are incorporated
Sole source impairment zone for surface water | 200-foot vegetative buffer if biosolids are not incorporated
Private well | 150 feet
Public water supply well, spring, or intake | 500 feet
Conduit to groundwater | 200 feet
School, institution, business, or occupied residence | 750 feet
Public right-of-way and property boundaries | 50 feet
Irrigation conveyance | 10 feet
Management requirements in Sect. 312.44

## Slide 22
What Other Requirements are in Place for Application of Biosolids?
Groundwater
Groundwater should be more than 3 feet below ground surface for soil with low permeability Groundwater should be more than 4 feet below ground surface for soil that is highly permeable Apply biosolids uniformly across site
Management requirements in Sect. 312.44
Ecological
Application should not harm threatened or endangered species or destroy critical habitat Do not apply when land is flooded, frozen, or snow-covered to prevent impacts to wetlands

## Slide 23: How are Biosolids Monitored?
Monitoring of biosolids for metals, pathogen density, and vector attraction reduction depends on the amount of biosolids applied per year. Monitoring frequency is presented below. Monitoring may be increased or reduced after 2 years by TCEQ.
Monitoring requirements in Sect. 312.46
Amount* (metric tons per 365- day period [dry weight]) | Frequency
0 to less than 290 | once per year
290 to less than 1,500 | once per quarter
1,500 to less than 15,000 | once per 60 days
15,000 or greater | once per month
* Based on amount of bulk biosolids land applied or the amount of biosolids received by a person who prepares the biosolids for sale or give away in a bag or other container for land application

## Slide 24: What Testing is Required for Farmland?
Permits or registrations specify the testing requirements.
Testing frequency should consider common testing done at farmland for determining crop needs, soil pH, regulated metals, and other parameters.
Testing is required at most once every five years.
TCEQ can require more frequent testing as appropriate based on specific conditions.
Management requirements in Sect. 312.47 and 312.48

## Slide 25
TCEQ Oversight

## Slide 26: What Recordkeeping and Reporting is Required?
Generators of biosolids maintain records for:
Metals concentrations in biosolids;
Description of how pathogen requirements are met;
Description of how vector attraction requirements are met; and
Certifications that vector attraction and pathogen requirements have been met.
When applying biosolids through the notification process, the following information is recorded and reported to TCEQ annually:
Description of how management practice requirements are met for each location where biosolids are applied
Location and size of area of where biosolids are applied
Amount of biosolids applied to each site
Date and time biosolids are applied to each site
Description of how vector attraction requirements are met
Metal concentrations and total metals applied
Certification that vector attraction and pathogen requirements have been met
Management requirements in Sect. 312.47 and 312.48

## Slide 27: Which TCEQ Staff Monitor Are Responsible for Overseeing Reuse of Biosolids?
Permitting staff
Technical review for permits, notifications, and registrations
Provide technical assistance with permitting
Work with reporting and rule making
Legal Staff
Provide expertise on both state and federal regulations to permitting staff, the regulated community, and the public
Field Operations Investigators
Conduct site assessment evaluation for proposed sites
Inspect sites annually
Investigate public complaints

## Slide 28
Key Definitions

## Slide 29
Agricultural land – Land on which food, feed for animals, or fiber (like cotton) is grown.
Key
Definitions
Agricultural management unit – Area of agricultural land that has defined boundaries like a road, river or fence and is usually growing the same crop. A single farm could be an agricultural management unit.
Agronomic rate – Amount of nitrogen needed to support crop growth that won’t result in extra nitrogen that may move to groundwater it it is unused by the crop.
Beneficial use – Application of biosolids, water treatment residuals, or domestic septage below the agronomic rate.
Annual metal loading – The maximum amount of a metal that could be applied to land in 365 days.
Cumulative metal loading rate – The maximum amount of metal that may be applied to any specific area.
Domestic septage – Either a liquid or solid material removed from a septic system that does not include material from commercial or industrial sources or grease
Grease/grit trap waste – Specific collectors in place to collect waste from food services, automotive repair and service, laundries, and other similar operations

## Slide 30
Key
Definitions
Land application unit – An area where biosolids are applied onto or in soil within 5 feet of the surface
Land application – Spraying or spreading of biosolids, domestic septage, or water treatment residuals to condition the soil or fertilize crops. It can also include injection beneath the grounds surface.
Stabilization – Biological or chemical treatment processes that minimize issues from breakdown of organic compounds.
Temporary storage – Storage of waste regulated approved in writing by the agency.
Treat or treatment – Preparation of sewage sludge for final use or disposal, which includes stabilization, addition of materials to control pathogens and vectors, and dewatering.
Vector attraction - The characteristic of sewage sludge, biosolids, and domestic septage that attracts rodents, flies, mosquitoes or other organisms capable of transporting infectious agents.
Sole Source Surface Drinking Water Supply – Surface water that is sole source of supply of a public water supply system

## Slide 31
Notice
This information package provides general information regarding the regulation of biosolids in Texas but is not intended to precisely reflect all the details and requirements of the regulations.
For any questions regarding specific regulatory requirements, the reader is directed to the Texas Commission on Environmental Quality Regulations, Chapter 312 – Sludge Use, Disposal, and Transportation.